## Slide 1: Electronics and System Integration for Large-Area Pico-second Photodetectors
Henry Frisch, Enrico Fermi Institute, Univ. of Chicago
For Eric Oberla and the LAPPD Collaboration
See also the talks by Andrey Elagin, Ossie Siegmund, and Junqi Xie

## Slide 2: Outline
Motivation for fast-timing and large area (Need)
(4 min)
MCP Package as integrated HV DC electrical circuit; anode and waveform sampling as integrated RF electrical circuit (4 min)
Waveform sampling and Anode Details (6 min)
Outlook- challenges and Opportunities (1 min)
Acknowledgements- Eric Oberla for the opportunity to talk, LAPPD collaborators, Howard Nicholson and the DOE HEP, ANL Management, and the NSF.

## Slide 3: Colliders:
Approach: measure the difference in arrival times of photons and charged particles which arrive a few psec later.
Light source is Cherenkov light in the window/radiator.
Benefit: Discoveries in signatures not possible now
Need: 1) identify the quark content of charged particles
2) vertex photons
(Note: conventional TOF resolution is 100 psec -factor of 100 worse than our goal= 1” is 100 psec, so need a small scale-length).
Theme: extract all the information in each event (4-vectors)

## Slide 4
Example need- Higgs to gamma-gamma at the LHC - tie the photons to the correct vertex, and more precisely reconstruct the mass of the pair

## Slide 5: Neutrino Physics
Approach: measure the arrival times and positions of photons and reconstruct tracks in water
Benefit: Factor of 5 less volume needed, cost.
Need: lower the cost and extend the reach of large neutrino detectors
Competition- large PMT’s, Liquid Argon

## Slide 6: Can we build a photon TPC?
Work of Matt Wetstein (Argonne,&Chicago) in his spare time (sic)

## Slide 7: Medical Imaging (PET)
Need: 1) much lower dose rate
2) faster through-put
3) real-time feedback (therapy as well as diagnosis)
Approach: precise Time-of-Flight, sampling, real-time adaptive algorithms in local distributed computing, use much larger fraction of events and information
Benefit: higher resolution, lower dose to patient, less tracer production and distribution, new hadron therapy capabilities
Competition: Silicon PMT’s

## Slide 8: Reconstructing the vertex space point: Simplest case- 2 hits (x,y) at wall
T1, X1, Y1
T2, X2, Y2
Vertex (e.g. p0->gg)
Tv, Xv, Yv, Zv
Photon 1
Photon 2
Detector Plane
One can reconstruct the vertex from the times and positions- 3D reconstruction
E.g. for KOTO (Prof. Wah’s expt at JPARC)

## Slide 9: Cherenkov-sensitive Sampling Quasi- Digital Calorimeters
A picture of an em shower in a cloud-chamber with ½” Pb plates (Rossi, p215- from CY Chao)
A `cartoon’ of a fixed target geometry such as for JPARC’s KL-> pizero nunubar (at UC, Yao Wah) or LHCb

## Slide 10: Tile-Tray Integrated Design
Because this is an RF-based readout system, the geometry and packaging are an integral part of the electronic design
The design is modular, with 8”-square MCP sealed vacuum tubes (`tiles’) with internal strip-lines capacitively coupled to a ground plane (tray) that also holds the electronics.

## Slide 11: The Half-Meter-Squared SuperModule
A `tile’ is a sealed vacuum-tube with cathode, 2 MCP’s, RF-strip anode, and internal voltage divider
HV string is made with ALD
A `tray’ holds 12 tiles in 3 tile-rows
15 waveform sampling ASICS on each
end of the tray digitize 90 strips
2 layers of local processing (Altera)
measure extract charge, time,
position, goodness-of-fit

## Slide 12: How Does it Work?
Requires large-area, gain > 107, low noise, low-power, long life, 
(t)<10 psec, (x) < 1mm, and low large-area system cost
Realized that an MCP-PMT has all these but large-area, low-cost:
(since intrinsic time and space scales are set by the pore sizes- 2-20µ)
window
Photocathode on inside of window
Pair of micro-channel plates
RF strip-line anode
Incoming charged particle
Photo-electron
from cathode
Radiated Cherenkov photon
Output pulse of 107 electrons

## Slide 13: Incom Micropore Substrate
.075”
~150 20m pores
INCOM glass substrate
Incom.inc, Charlton Mass
80 million 20-micron pores in an 8”-sq plate
65% open-area ratio; 1.2mm thick (L/D=60)

## Slide 14: Waveform Sample On Ends of Strips
Eric Oberla slide from ANT11

## Slide 15: Extract time, charge, shape each end
Eric Oberla slide from ANT11

## Slide 16: Extract time, position of pulse using time from both ends
Eric Oberla slide from ANT11

## Slide 17: SuperModule Mockup
Real 8” glass tile package parts- anode, side-wall, window (sic)
`Innards’ stack of 2 MCP’s +3 spacers+anode+window under test
Have read out through from AC card through full DAQ chain to PC

## Slide 18: Developing and Testing the Electronics, Anodes, and DAQ
Eric Oberla (grad student) and Craig Harabedian (engineer) working on the Tray layout and cabling

## Slide 19: Digital Cards and Central Card
Present readout to PC and Nvidia GPU is via USB;
Ethernet hardware is on boards- later

## Slide 20: Analog Card to Digital Card
Can be direct connection (shown) or cable

## Slide 21: Anode Testing for ABW, Crosstalk,..
Network Analyzer Tile Anode
Herve’ Grabas, Razib Obaid, Dave McGinnis

## Slide 22: Anode Testing for ABW, Crosstalk,..
Razib Obaid
Crosstalk
ABW

## Slide 23: Simulation of Resolution vs abw
Jean-Francois Genat (NIM)
Brown line: 10 Gs/sec (we’ve done >15);
1.5 GHz abw ( we’ve done 1.6); S/N 120 (N=0.75mv, S is app specific)
This (brown) line
This (brown) line
1 ps

## Slide 24: The PSEC4 Waveform Sampling ASIC
PSEC4: Eric Oberla and Herve Grabas; and friends…
Eric Oberla, ANT11

## Slide 25
PSEC-4 ASIC
6-channel “oscilloscope on a chip” (1.6 GHz,10-15 GS/s)
Evaluation board uses USB 2.0 interface + PC data acquisition software
LAPPD Collaboration
Eric Oberla, ANT11

## Slide 26: 6-channel `Scope-on-a-chip’
20 GS/scope
4-channels (142K$)
17 GS/PSEC-4 chip
6-channels ($130 ?!)
Real digitized traces from anode
Designed by Eric Oberla (UC grad student)
working in EDG
with EDG tools
and zeitgeist

## Slide 27
PSEC-4 Performance
Digitized Waveforms
Input: 800MHz, 300 mVpp sine
Sampling rate : 10 GSa/s
Sampling rate : 13.3 GSa/s
Only simple pedestal correction to data
As the sampling rate-to-input frequency ratio decreases, the need for time-base calibration becomes more apparent (depending on necessary timing resolution)
Eric Oberla, ANT11

## Slide 28: Digitization Analog Bandwith
ABW~1.6GHz
3 db loss
PSEC4: Eric Oberla and Herve Grabas+ friends…
Eric Oberla, ANT11

## Slide 29: Noise (unshielded)
PSEC4: Eric Oberla and Herve Grabas+ friends…
RMS=755 microvolts
Full-Scale ~1.2 volts (expect S/N>=100, conservatively)
Eric Oberla, ANT11

## Slide 30: Opportunities:Can we go deep sub-picosec?: the Ritt Parameterization (agrees with JF MC)
S/N, fZ: DONE
abw: NOT YET
100 femtosec
Stefan Ritt slide, doctored

## Slide 31: Challenges
Photocathode- vacuum transfer (vs not)
Top seal- indium (vs frit, other, metal for neutrons)
Getter, long-time vacuum (6.4 m2/plate)
Commercialization (risk abatement=$$)
Talent- esp. career paths for young ones (anything that takes more than 3 yrs is a major problem)
Identifying the first adopters
Continued funding

## Slide 32: More Information on LAPPD:
Main Page: http://psec.uchicago.edu (has the links to the Library and Blogs)
Library: Workshops, Godparent Reviews, Image Library, Document Library, Links to MCP, Photocathode, Materials Literature, etc.;
Blog: Our log-book- open to all (say yes to certificate Cerberus, etc.)- can keep track of us (at least several companies do);

## Slide 33
The End

## Slide 34: Backup slides

## Slide 35: Parallel Efforts on Specific Applications
.
LAPD Detector Development
PET
(UC/BSD, UCB, Lyon)
Collider
(UC, ANL,Saclay.
Mass Spec
Andy Davis, Mike Pellin, Eric Oberla
Non-proliferation
LLNL,ANL,UC
Drawing Not To Scale (!)
ANL,Arradiance,Chicago,Fermilab, Hawaii,Muons,Inc,SLAC,SSL/UCB, UIUC, Wash. U
Explicit strategy for staying on task-
Multiple parallel cooperative efforts
All these need work- naturally tend to lag the reality of the detector development
Neutrinos
(Matt, Mayly, Bob, John, ..; Zelimir)
Muon Cooling
Muons,Inc
(SBIR)
K->pnn
JPARC

## Slide 36
The up and down quarks are light (few MeV), but one can trace the others by measuring the mass of the particles containing them. Different models of the forces and symmetries predict different processes that are distinguishable by identifying the quarks. Hence my own interest.
Nico Berry (nicoberry.com)
Q=2/3
Q=-1/3
The unexplained structure of basic building blocks-e.g. quarks
M=175,000 MeV
M=4,500 MeV
M~2 MeV
M=1750 MeV
M=300 MeV
M~2 MeV

## Slide 37: ALD &Integration tests at ANL
Argonne Atomic Layer Deposition and Test Facilities
In situ measurements of R (Anil)
Femto-second laser time/position measurements (Matt, Bernhard, Razib, Sasha)
33 mm development program
8” anode injection measurements
Anil Mani and Bob Wagner

## Slide 38: Daniel Boone
Proposal (LDRD) to build a little proto-type to test photon-TPC ideas and as a simulation testbed
`Book-on-end’ geometry- long, higher than wide
Close to 100% coverage so bigger Fid/Tot volume
Dx, Dy << 1 cm
Dt < 100 psec
Magnetic field in volume
Idea: to reconstruct vertices, tracks, events as in a TPC (or, as in LiA).
n
2 m
2 m
1 m
caps

## Slide 39: Simplifying MCP Construction
Chemically produced and treated Pb-glass does 3-functions:
Provide pores
Resistive layer supplies electric field in the pore
Pb-oxide layer provides secondary electron emission
Conventional Pb-glass MCP
OLD
Incom Glass Substrate
NEW
Separate the three functions:
Hard glass substrate provides pores;
Tuned Resistive Layer (ALD) provides current for electric field (possible NTC?);
Specific Emitting layer provides SEE

## Slide 40: First measurements of gain in an ALD SEE layer at the APS laser test setup (Bernhard Adams, Matthieu Cholet, and Matt Wetstein)
Testing Group: Bernhard Adams, Matthieu Cholet, and Matt Wetstein at the APS, Ossy Siegmund’s group at SSL
LAPPD Preliminary
(very)
MCP and Photocathode Testing
N. B.!

## Slide 41: Psec Large-area Micro-Channel Plate Panel (MCPP)- LDRD proposal to ANL (with Mike Pellin/MSD)
Front Window and Radiator
Photocathode
Pump Gap
High Emissivity Material
Low Emissivity Material
`Normal’ MCP pore material
Gold Anode
50 Ohm Transmission Line
Rogers PC Card
Capacitive Pickup to Sampling Readout
N.B.- this is a `cartoon’- working on workable designs-join us…

## Slide 42: KL to pizero nu-nubar

## Slide 43: The Large-Area Psec Photo-Detector Collaboration

## Slide 44: Microchannel Plates-2
Argonne ALD and test Facilities
In situ measurements of R (Anil)
Femto-second laser time/position measurements (Matt, Bernhard, Razib, Sasha)
33 mm development program
8” anode injection measurements
Anil Mani and Bob Wagner

## Slide 45: Microchannel Plates-3
SSL (Berkeley) Test/Fab Facilities
Ossy Siegmund, Jason McPhate, Sharon Jelenski, and Anton Tremsin-
Decades of experience
(some of us have decades of inexperience?)

## Slide 46: Microchannel Plates-4b
Noise (bkgd rate).
<=0.1 counts/cm2/sec; factors of few > cosmics (!)
Ossy Siegmund, Jason McPhate, Sharon Jelinsky, SSL/UCB
Performance:

## Slide 47: Microchannel Plates-4d
Performance: burn-in (aka `scrub’)
Measurements by
Ossy Siegmund,
Jason McPhate,
Sharon Jelinsky, SSL/UCB
Typical MCP behavior- long scrub-times
Measured ANL ALD-MCP behavior
(ALD by Anil Mane, Jeff Elam, ANL)

## Slide 48: Photocathodes Subject of next talk by Klaus- touch on here only briefly
LAPPD goal- 20-25% QE, 8”-square
2 parallel efforts: SSL (knows how), and ANL (learning)
ANL
Optical stand
First cathodes made at ANL
Burle commercial
equipment

## Slide 49: Hermetic Packaging
Top Seal and Photocathode- this year’s priority
Commercial RFI for 100 tiles
(Have had one proposal for 7K- 21K tiles/yr)
Tile Development Facility at ANL
Production Facility at SSL/UCB
3 parallel paths

## Slide 50: Matt Wetstein; ANL&UC
Works on GEANT events too

## Slide 51: Sampling calorimeters based on thin cheap photodetectors with correlated time and space waveform sampling
Proposal: Alternating radiator and cheap 30-50 psec thin planar mcp-pmt’s on each side (needs simulation work)
    Bill Moses (Lyon)

## Slide 52: A `Quasi-digital’ MCP-based Calorimeter
Electron pattern (not a picture of the plate!)- SSL test, Incom substrate, Arradiance ALD. Note you can see the multi’s in both plates => ~50 micron resolution
Note- at high gain the boundaries of the multi’s go away
Idea: can one saturate pores in the the MCP plate s.t.output is proportional to number of pores. Transmission line readout gives a cheap way to sample the whole lane with pulse height and time- get energy flow.
Oswald Siegmund, Jason McPhate, Sharon Jelinsky, SSL (UCB)

## Slide 53: FY-08 Funds –Chicago Anode Design and Simulation (Fukun Tang)

## Slide 54: MCP+Transmission Lines Sampled at Both Ends Provide Time and 2D Space
8” Tiles
10-15 GS/sec Waveform Sampling ASICS
Field Programable Gate Arrays
(not as shown- PC cards will be folded behind the panel- not this ugly…
Single serial Gbit connection will come out of panel with time and positions from center of back of panel

## Slide 55: Applications
SRI’s NABC Approach http: //www.itu.dk/~jeppeh/DIKP/NABC.pdf (sic- Denmark?)

## Slide 56: The 4 `Divisions’ of glass LAPPD
CV
CV
Hermetic Packaging
CV
CV
Electronics/Integration
MicroChannel Plates
Photocathodes
This talk
See (hear) Klaus Attenkofer’s talk
See Ossy’s talk
See Bob Wagner’s talk

## Slide 57: LAPPD Performance
Fast Preconditioning
Low noise
400 micron resolution
(8” plate, anode, PSEC-4)
High Gain (>107)

## Slide 58: Signal- want large for S/N
We see gains > 107 in a chevron-pair
Ossy Siegmund, Jason McPhate, Sharon Jelinsky, SSL/UCB
ALD by Anil Mane and Jeff Elam, ANL

## Slide 59: SS
ss