## Slide 1: Design of a 8 Channel 40 GS/sec 20 mW/Channel Waveform Sampling ASIC in 65 nm CMOS
Jinseo Park2,
D. Braga1, F. Fahim1, N. J. Pastika1, P. M. Rubinov1, T. N. Zimmerman1,
T. England1, H. J. Frisch2, M. Heintz2, E. Oberla2, C. Poe2, Y. R. Yeung2,
C. Ertley3, N. Sullivan4,
E. Angelico5,
Hector Rico-Aniles6
1. Fermi National Accelerator Laboratory 2. University of Chicago 3. Southwest Research Institute 4. Angstrom Research Inc. 5. Stanford University 6. North Central College
Notes: Hi everyone. I’m Jin, and I will present the new chip we are developing for fast timing.

## Slide 2: Motivation: Detectors with ps level resolution
…WE ALSO NEED SUB-PS RESOLUTION FE ELECTRONICS!
Timing resolution for
200 pe =~5ps
Perazzini S, Ferrari F, Vagnoni VM, on behalf of the LHCb ECAL Upgrade-2 R&D Group. Development of an MCP-Based Timing Layer for the LHCb ECAL Upgrade-2
LAPPDTM, psec.uchicago.edu
Notes: Our research is motivated by a simple fact that there are particle detectors that are capable of achieving very good timing resolution of a scale of ps, such as Micro Channel Plate based Photo multiplyer tubes. We wanted to push the limits of these detectors so that the resolution of future experiments are not restricted by the timing resolution of detectors. (next) That is why we decided to aim for sub ps resolution in front end electronics.

## Slide 3: Primary goal
Achieve <1ps resolution in measuring the arrival time of LAPPD pulses.
But we also aim for a versatile chip, so that it is applicable to other fast-timing applications
Sample and Hold at very fast frequency, and then digitize the held voltage values using commercial ADC chips.

## Slide 4: PSEC5
Process | 65nm TSMC
Signal to Noise | 1000
Sampling Rate | 40GSa/s(5GSa/s)
Buffer Length | 6.4ns(204.8ns)
Analog Bandwidth | 5GHz
Channels/Chip | 8
Area | 2mm2
Max. Readout Rate | 40KHz
Institution | UChicago & Fermilab
Notes: PSEC5 is being designed in 65nm TSMC and consists of 16 channels. Each channel having 10-bit depth and 40 Gigasamples per second. It also has 5 Gigahertz analog bandwidth. The aim for peak power consumption is less than 20 milliwatts per channel.
In each channel,
(next)
Front end 5GHz buffer
(next)
Four fast banks
(next)
Single slow bank
(next)
Trigger logic with discriminator

## Slide 5: Schedule
Schematic / Simulation | Sep. 2023
Layout | Mar. 2024
Post Layout Simulation | Apr. 2024
Layout Optimization | Jul. 2024
Tapeout without package (Pre-production) | Sep. 2024
Testbench (Chip on Board) | Dec. 2024
Production | 2025
200x8 um
550 um
Core Layout
(Without Digital & Clock generation Block)

## Slide 6: Comparison with Oscilloscope
 | PSEC5 | Oscilloscope
Power/Channel | Low(20mW/Ch) | High
Output | Analog | Digital
Real Time | No(40k events/s) | Yes
Cost/Channel | Low | High
Input Voltage Buffer 5GHz
Sample and Hold Capacitors
(Discriminator Trigger)
Output Voltage Buffer 40MHz

## Slide 7: Point 1. Fast & Slow Banks
LAPPD event readout with a stripline anode
Notes: The first point of our chip is that it has separate fast and slow banks for the sake of versatility, and achieving both long buffer and good timing resolution. The slow bank captures the entire signal and is used as a timestamp. It is about 200ns long with about 1000 samples. Fast bank captures only the region of interest as it is only 1.6 nanoseconds long, but has a higher sampling rate so that the reconstruction algorithm can achieve better resolution. Since fast banks have higher power consumption, only up to one of the banks is running at any given time to reduce power consumption. Also, there is a separate counter per fast bank to record the trigger position.

## Slide 8
Chart: Time [ns]
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4 | 4.2 | 4.4000000000000004 | 4.5999999999999996 | 4.8 | 5 | 5.2 | 5.4 | 5.6 | 5.8 | 6
Signal (Slow Bank) | 0.00053624 | 0.0028827 | 0.010784 | 0.022583 | 0.062327 | 0.1382 | 0.28673 | 0.49189 | 0.73028 | 0.92587 | 1.0061 | 0.93102 | 0.73772 | 0.51052 | 0.33758 | 0.27169 | 0.33537 | 0.51282 | 0.74075 | 0.93391 | 1.0059 | 0.92497 | 0.72881 | 0.48882 | 0.28197 | 0.13886 | 0.063164 | 0.02677 | 0.010479 | 0.0025898 | 0.0088129
Threshold | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
4 Fast Banks
  64×4 samples
  1.6ns×4 of sampling window
  High power consumption
  Run sequentially
Slow Bank
  1024 samples
  204.8ns of sampling window
  Low power consumption
  Fast banks are triggered within the sampling window
10bit counter
A
B
Chart: Time [ns]
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4 | 4.2 | 4.4000000000000004 | 4.5999999999999996 | 4.8 | 5 | 5.2 | 5.4 | 5.6 | 5.8 | 6
Fast Bank A | 0.49048 | 0.73025 | 0.92675 | 1.0058 | 0.93032 | 0.73916 | 0.50816 | 0.33716
Fast Bank B | 0.51585 | 0.73608 | 0.9294 | 1.0054 | 0.92325 | 0.73551 | 0.49321 | 0.28063
Propagation delay ~800ps
Hold delay ~800ps
Fast Bank Usage Example
Notes: The first point of our chip is that it has separate fast and slow banks for the sake of versatility, and achieving both long buffer and good timing resolution. The slow bank captures the entire signal and is used as a timestamp. It is about 200ns long with about 1000 samples. Fast bank captures only the region of interest as it is only 1.6 nanoseconds long, but has a higher sampling rate so that the reconstruction algorithm can achieve better resolution. Since fast banks have higher power consumption, only up to one of the banks is running at any given time to reduce power consumption. Also, there is a separate counter per fast bank to record the trigger position.

## Slide 9: Fast sampling - interleaved
0˚ 5GHz Clock
90˚
180˚
270˚
~200um
Notes: This is how four fast banks are arranged in each channel. Each fast bank is four 16-sample columns interleaved, each sampling at 10GHz and a phase of zero, ninety, one hundred and eighty, and two hundred and seventeen degrees. This results in an effective 40GHz sampling rate. The green signal line comes from the left of the figure, while the purple clock line comes from the right of the figure. The arrangement of the columns is chosen so that every column retains the maximal signal bandwidth. (next) the length of the signal line is an important consideration for the analog bandwidth.

## Slide 10: Layout of a single column (16 cells)
Size:
Capacitor: 35fF
Sampling Switch
2.5V NMOS
Size:
Notes: This is a picture presenting a single column with 16 cells. We will have a 4x4 array of these column in a single channel. It’s size is 45 times 25 micrometers. The capacitance of each cell is 35femtofarads. (next) The sampling switch we use is shown in the layout, which is 2.5V nMOS with 4 micrometers wide and 280 nanometers long.

## Slide 11: Switching Drift
The value of a capacitor drifts while it switches off from the signal line.
Drift consists of switch gate charge injection, which is a fixed value and is calibratable, and resistive drift, which is dependent on signal V.
It is essential to keep the
[Sample  Hold] transition time low.
NMOS instead of CMOS for the sampling switch!
Switch Gate V
Signal
Capacitor V
(Sample)
(Hold)
Transition time
Drift
Notes: Switch gate charge injection: due to capacitance between gate of the switch and the signal route
Resistrive drift: due to resistance of the switch while it is switching off.

## Slide 12: Voltage Level Shifter
Notes: Switch gate charge injection: due to capacitance between gate of the switch and the signal route
Resistrive drift: due to resistance of the switch while it is switching off.

## Slide 13: Point 2. Sampling Time Uncertainty
At <1ps timing resolution region, it is a dominant component of the overall uncertainty.
Previous Chip PSEC4 employed Delay Locked Loop (DLL) to control sampling switches.
Process Variation is a major source of systematic timing uncertainty.
Monte Carlo results based on Delagnes, arXiv:1606.05541
Diminishing return above 10 ENoB
Notes: We concluded that in terms of timing resolution, the return diminishes as Signal to noise ratios reach 1/1000 or 10 effective bits. (next) In this region, sampling time jitter has a greater impact on the overall timing resolution.
Time differences between samples are determined by a voltage-controlled delay line, which is an array of transistors, usually MOSFETs, in which a signal propagates through the array at a desired rate.
However, no chip manufacturing process is perfect, so each element of the VCDL has a different time offset.
It is necessary to measure each time offset to correctly sample a signal.

## Slide 14: PSEC4 ASIC(2014)
E. Oberla, H. Frisch, K. Nishimura, G. Varner, arxiv.org/abs/1309.4397
12-bit depth
6 channel/chip
5ps resolution
130nm IBM 8RF
E. Oberla, Talk at Workshop on Picosecond Photon Sensors, Clermont-Ferrand,
http://lappddocs.uchicago.edu/documents/243
Notes: This is a brief structure of ASIC we have been using for almost a decade now. The signal goes into the chip from the left. First, its DC component is removed and set to a constant voltage, V_ped, which can be controlled by an FPGA for example. Then there is an array of capacitors, where each capacitor represent a sample. The last stage of the chip is Wilkinson ADC, where the voltage in each capacitor is compared with a ramp and converted to a 12 bit number.

## Slide 15
1. Measure many events of a sine wave.
2. Sum vs. Difference of two adjacent samples, over all events, form an ellipse.
3. Time offset can be determined from the coefficients.
determined by eccentricity and rotation.
PSEC4 Measurement
Chart: 
 | 0.5 | 0.63049 | 0.735 | 0.79272 | 0.79215 | 0.73342 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504
Chart: 
 | 0.79272 | 0.79215 | 0.73342 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378
Chart: 
 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378 | 0.79097 | 0.73022 | 0.62364
Chart: 
 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378 | 0.79097 | 0.73022 | 0.62364 | 0.49243 | 0.36274 | 0.26037
Input Voltage
Time
Event 1
Event 2
Event 3
Event 4
Low SNR  fainter, more spread curve.
Nonlinearity  distorted curve
sin(ωt+Δt)+sin(ωt)
sin(ωt+Δt)-sin(ωt)
Notes: To reduce the sample time uncertainty, we have developed a method to measure the time offset of each sample.
1. Measure many events of a sine wave.
2. Plot Summation vs. Difference of two adjacent samples, over all events, should form an ellipse.
3. Time offset can be determined from the coefficients.
The diagram explains which event corresponds to which dot in the ellipse plot, which is the actual measurement data of PSEC4.
When you think about it, the plot does not have to be on two adjacent samples, but samples that are m samples apart. This way the effect of voltage noise of each sample on the time offset is smaller.
In other words, the sampled curve is more like a smooth ellipse as m gets larger.
However, the time difference cannot be larger than one fourth of the period of the sine wave, which in our case corresponded to m equal to about 10.
When we look at the right ellipse plot,
Higher voltage Noise results in a fainter, more spread curve.
The nonlinearity of the overall system results in a distorted curve

## Slide 16: Sample Time Distribution of PSEC4
Notes: To reduce the sample time uncertainty, we have developed a method to measure the time offset of each sample.
1. Measure many events of a sine wave.
2. Plot Summation vs. Difference of two adjacent samples, over all events, should form an ellipse.
3. Time offset can be determined from the coefficients.
The diagram explains which event corresponds to which dot in the ellipse plot, which is the actual measurement data of PSEC4.
When you think about it, the plot does not have to be on two adjacent samples, but samples that are m samples apart. This way the effect of voltage noise of each sample on the time offset is smaller.
In other words, the sampled curve is more like a smooth ellipse as m gets larger.
However, the time difference cannot be larger than one fourth of the period of the sine wave, which in our case corresponded to m equal to about 10.
When we look at the right ellipse plot,
Higher voltage Noise results in a fainter, more spread curve.
The nonlinearity of the overall system results in a distorted curve

## Slide 17
Timing uncertainty reduced by an optimized LC-oscillator based PLL
J. Prinzie, J. Christiansen, P. Moreira, M. Steyaert and P. Leroux, "Comparison of a 65 nm CMOS Ring- and LC-Oscillator Based PLL in Terms of TID and SEU Sensitivity," in IEEE Transactions on Nuclear Science, vol. 64, no. 1, pp. 245-252, Jan. 2017.
From abstract: “Both independent PLLs have identical loop dynamics to allow a fair comparison … Furthermore these circuits consume the same amount of power. The PLLs were processed in a commercial 65 nm CMOS technology.”
Ring: 5.6ps jitter
LC: 0.325ps jitter
Notes: As I said before, we are currently using ring osc for the phase locked loop for the Voltage controlled delay line
This can be replaced to LC oscillator based phased locked loop to achieve better timing uncertainty.

## Slide 18: 5GHz Dual Edge Triggered D Flip-Flop
Still, we expect to use similar calibration technique as PSEC4
5GHz
To each sampling switches
Notes: To reduce overall sampling jitter and prevent jitter from cumulating, we used a d flip flop per sample to generate writing strobe, opposed to a delay line. The schematic of a single d flip flop is shown on the screen. In 65nm, it is fast enough to work reliably at 10GHz.

## Slide 19: Performance Measurement
Same signal fed into two different channels of the same readout board.
1. measured for many events.
2. Distribution of acquired.
Depends on the source
  Sin
  Pulse/square
Depends on algorithm determining .
PSEC4
Chart: Ch. 1 Voltage[V]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: Ch. 1 Voltage[V]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: Time[ns]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: Time[ns]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
t=0 when the VCDL loop starts
[ps]
# of Events
Notes: The way we measure the performance of the chip is to measure *time distribution of the sampled signal when sampling the same waveform many times.*
We set up an experiment where Same signal is fed into two different channels of the same readout board.
Then, delta t , the phase difference, is measured for each event the way described in figure on the right side.
1. measured for many events.
2. Distribution of acquired.
However, one should be aware that delta t depends on the signal source and the algorithm determining where the pulse starts.
The way we measure the performance of the chip is to measure *time distribution of the sampled signal when sampling the same waveform many times.*
We set up an experiment where Same signal is fed into two different channels of the same readout board.
Then, delta t , the phase difference, is measured for each event the way described in figure on the right side.
1. Δ𝑡 measured for many events.
2. Distribution of Δ𝑡 acquired.
However, one should be aware that delta t depends on the signal source and the algorithm determining where the pulse starts.

## Slide 20: Summary
PSEC5 is a reliable, reusable, and cost-efficient waveform sampling ASIC.
  Lower power consumption and dead time
  Avails various methods of external calibration
  High channel count per chip
The fast-slow architecture of the chip makes it relatively versatile
  Long time window (204.8 ns) per event
  While also achieving high timing resolution on regions of interest (6.4 ns)
It can easily be incorporated as a front end of any detector system which requires <1ps timing resolution.
THANK YOU FOR YOUR ATTENTION!

## Slide 21: Trigger via CFD Logic
Diagram
Chart: 
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: 
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2

## Slide 22: Switch Comparison(@width 32um+80um)
 | Cmos | Cmos-2.5v | Cmos-lvt | Nmos | Nmos-2.5v | Nmos-lvt | Nmos-hvt
V Range | 1.2v | 2.5v | 1.2v | <1.2v* | <2.5v* | <1.2v* | <1.2v*
Rel. Gate capacitance | 100+250 | 450+1125 | 95+240 | 100*** | 450 | 95 | 
Cutoff Freq** | 5GHz | 27GHz | 18GHz | 8GHz | 48GHz | 27GHz | 600MHz
Length | 60n | 280n | 60n | 60n | 280n | 60n | 60n
Phase @ 5GHz | -36˚ | -9˚ | -13˚ | -27˚ | -5˚ | -9˚ | 
Hold Time**** | 68ns | >10us | 1.7ns | 71ns | >20us | 2.6ns | 2u
*Higher impedance as the signal voltage reaches vdd, noticeable at V>0.6vdd
**(Capacitor V Amplitude / Signal V Amplitude) reaches 0.7. ss corner, 0.1v amp
***~2fF C_ox
****ff corner, 10% decay after sampling vdd.

## Slide 23: Template Fitting
In template fitting,
1606.05541v1.pdf (arxiv.org)

## Slide 24: ODR w/ Monte Carlo
In template fitting,

## Slide 25: Point 1. SNR

## Slide 29: PSEC5 Design decisions

## Slide 30: Factors determining SNR()
Artifact
  Memory effect
  Leak current
  Crosstalk
Coupling & Supply noise
  Input-output coupling
  Clock coupling (Often reproducible)
  Power Supply Rejection Ratio (PSRR)
Device
  kT/C (Nyquist)
  Buffer/Filter noise
  Flicker noise (below ~MHz)
ADC readout noise

## Slide 31: Factors less relevant to SNR()
Artifact
  Charge injection depending on (Reproducible)
Distortion
  Due to nonuniform over voltage range (Reproducible)
  Due to nonzero shutoff time (Reproducible)
  Due to low bandwidth (Reproducible)

## Slide 32: Factors determining Jitter()
LC-PLL jitter
Clock distribution
Shift register jitter
  PSRR
Uncertainty of the off-chip calibration of shift register process variation.
  Given that we use the sine wave fitting method to calibrate the PV,
    3 Distortion factors discussed before matters.

## Slide 33: Advantage of 65nm technology
Speed vs Leakage
Cost vs Area

## Slide 34: Key considerations
Impedance when the switch is closed.
  Introduces frequency-dependent harmonic distortion into the final digitized waveform, which is not trivial to calibrate.
Nyquist(thermal) noise of the sampling capacitor
Power rail noise:
  1. Switch gate  Capacitor
  2. CC Follower current source  ADC Readout
Voltage range – at least 1000 times the noise level to achieve 10-bit precision.
Power consumption

## Slide 35: Minor considerations
Capacitive coupling between the signal transmission line and the sampling capacitor
  Reason: could be mitigated by adding another switch in front of the signal line which switches off when the ADC is reading.
Hold time of the capacitor; Leak current through the switch
  Reason: Leak current seems low in 2.5V transistors. Requires discussion.
Charge injection from the switch
  Reason: Can be calibrated by capacitor-wise voltage-ADC curve measurement.

## Slide 36
Nominal sampling rate | 1.2v DFF (BW = 8GHz) | 2.5v DFF (BW = 48GHz) | 1.2v DLL (BW = 8GHz) (Jitter = 1ps) | 2.5v DLL (BW = 48GHz)
5GHz | Simulation says the low-power design of DFF can cover this frequency. Rising edge of the clock is ~80ps. | Requires simulation. | Trivial. | Works in simulation.
10GHz | I was not able to get any design of DFF run at this frequency. Can utilize 10GHz PLL which is under development(2024?). | Requires simulation, but design running at this frequency and full voltage range is rare. Can utilize 10GHz PLL with additional complications involved. | Former chip (PSEC4), sampling time jitter measured at ~1ps @ DLL loop length 25ns & 256 delay elements. | Works in simulation. (Optimization TBD)

## Slide 38: Fast & Slow sampling
Fast Bank: 4 of them
  64 samples
  1.6ns of sampling window
  High power consumption
  Triggered one by one
Slow Bank
  1024 samples
  204.8ns of sampling window
  Low power consumption
  Fast banks are triggered within the sampling window

## Slide 39: Dynamic range of PSEC5
Single transistor FE Buffer
2.5V NMOS switch
Read Buffer

## Slide 40
Category | Factor | Simulation of 2.5v nMOS 280nmx4um, 50fF
Artifact | Memory effect | None if sampling time > 7RC (~100ps)
 | Leak current | <1mV after 1us
 | Crosstalk | N/A(<10mV in PSEC4)
Signal path coupling | High impedance node noises | N/A (Post-layout)
 | Input-output coupling | N/A (Post-layout)
 | Clock coupling | N/A (Post-layout)
 | PSRR | N/A
 | kT/C (Nyquist) | 0.3mV
 | Buffer & Filter noise | N/A
Distortion | nonuniform | THD = 1% @ 250MHz
 | nonzero shutoff time | 20ps, THD = 2% @ 250MHz
 | bandwidth | 9GHz
 | PLL jitter | N/A
 | Clock distribution jitter | N/A
 | Shift register jitter | N/A
 | Uncertainty of the off-chip calibration of PV | TBD
Meta | Power consumption per channel | 3.2mW x 5
 | Area per channel | (~300)*(16*16+1024) =
Category | Factor | Simulation of 2.5v nMOS 280nmx4um, 50fF
Artifact | Memory effect | None if sampling time > 7RC (~100ps)
 | Leak current | <1mV after 1us
 | Crosstalk | N/A(<10mV in PSEC4)
Signal path coupling | High impedance node noises | N/A (Post-layout)
 | Input-output coupling | N/A (Post-layout)
 | Clock coupling | N/A (Post-layout)
 | PSRR | N/A
 | kT/C (Nyquist) | 0.3mV
 | Buffer & Filter noise | N/A
Distortion |  | THD = 1% @ 250MHz
 | nonzero shutoff time | 20ps, THD = 2% @ 250MHz
 | bandwidth | 9GHz
 | PLL jitter | N/A
 | Clock distribution jitter | N/A
 | Shift register jitter | N/A
 | Uncertainty of the off-chip calibration of PV | TBD
Meta | Power consumption per channel | 3.2mW x 5
 | Area per channel | 

## Slide 41
Category | Factor | Dummy switch
Artifact | Memory effect | No effect
 | Leak current | No effect
 | Crosstalk | No effect
Signal path coupling | High impedance node noises | No effect
 | Input-output coupling | No effect
 | Clock coupling | No effect
 | PSRR | No effect
 | kT/C (Nyquist) | No effect
 | Buffer & Filter noise | No effect
Distortion | nonuniform | Greatly reduces
 | nonzero shutoff time | Reduces?
 | bandwidth | Increases
 | PLL jitter | No effect
 | Clock distribution jitter | No effect
 | Shift register jitter | Increases?
 | Uncertainty of the off-chip calibration of PV | ?
Meta | Power consumption per channel | Increases
 | Area per channel | Increases
Category | Factor | Dummy switch
Artifact | Memory effect | No effect
 | Leak current | No effect
 | Crosstalk | No effect
Signal path coupling | High impedance node noises | No effect
 | Input-output coupling | No effect
 | Clock coupling | No effect
 | PSRR | No effect
 | kT/C (Nyquist) | No effect
 | Buffer & Filter noise | No effect
Distortion |  | Greatly reduces
 | nonzero shutoff time | Reduces?
 | bandwidth | Increases
 | PLL jitter | No effect
 | Clock distribution jitter | No effect
 | Shift register jitter | Increases?
 | Uncertainty of the off-chip calibration of PV | ?
Meta | Power consumption per channel | Increases
 | Area per channel | Increases

## Slide 42
Category | Factor | Bootstrap
Artifact | Memory effect | No effect
 | Leak current | No effect
 | Crosstalk | No effect
Signal path coupling | High impedance node noises | No effect
 | Input-output coupling | No effect
 | Clock coupling | No effect
 | PSRR | No effect
 | kT/C (Nyquist) | No effect
 | Buffer & Filter noise | No effect
Distortion | nonuniform | Greatly reduces
 | nonzero shutoff time | Greatly reduces
 | bandwidth | Increases
 | PLL jitter | No effect
 | Clock distribution jitter | No effect
 | Shift register jitter | Increases?
 | Uncertainty of the off-chip calibration of PV | ?
Meta | Power consumption per channel | Increases
 | Area per channel | Increases
Category | Factor | Bootstrap
Artifact | Memory effect | No effect
 | Leak current | No effect
 | Crosstalk | No effect
Signal path coupling | High impedance node noises | No effect
 | Input-output coupling | No effect
 | Clock coupling | No effect
 | PSRR | No effect
 | kT/C (Nyquist) | No effect
 | Buffer & Filter noise | No effect
Distortion |  | Greatly reduces
 | nonzero shutoff time | Greatly reduces
 | bandwidth | Increases
 | PLL jitter | No effect
 | Clock distribution jitter | No effect
 | Shift register jitter | Increases?
 | Uncertainty of the off-chip calibration of PV | ?
Meta | Power consumption per channel | Increases
 | Area per channel | Increases

## Slide 43
Category | Factor | Differential
Artifact | Memory effect | No effect
 | Leak current | No effect (?)
 | Crosstalk | Partially cancelled
Signal path coupling | High impedance node noises | No effect
 | Input-output coupling | No effect
 | Clock coupling | Partially cancelled
 | PSRR | Partially cancelled
 | kT/C (Nyquist) | No effect (effectively 70%)
 | Buffer & Filter noise | No effect (effectively 70%)
Distortion | nonuniform | Canceled
 | nonzero shutoff time | Increases
 | bandwidth | No effect
 | PLL jitter | No effect
 | Clock distribution jitter | Increases
 | Shift register jitter | Increases + Mismatch (Design dependent)
 | Uncertainty of the off-chip calibration of PV | ?
Meta | Power consumption per channel | x2
 | Area per channel | x2
Category | Factor | Differential
Artifact | Memory effect | No effect
 | Leak current | No effect (?)
 | Crosstalk | Partially cancelled
Signal path coupling | High impedance node noises | No effect
 | Input-output coupling | No effect
 | Clock coupling | Partially cancelled
 | PSRR | Partially cancelled
 | kT/C (Nyquist) | No effect (effectively 70%)
 | Buffer & Filter noise | No effect (effectively 70%)
Distortion |  | Canceled
 | nonzero shutoff time | Increases
 | bandwidth | No effect
 | PLL jitter | No effect
 | Clock distribution jitter | Increases
 | Shift register jitter | Increases + Mismatch (Design dependent)
 | Uncertainty of the off-chip calibration of PV | ?
Meta | Power consumption per channel | x2
 | Area per channel | x2

## Slide 44: Factors determining
LAPPD & Pickup board
Distortion
  Due to nonuniform over voltage range (Negligible)
  Due to nonzero shutoff time (Negligible)
  Due to low bandwidth (Decreases slope)

## Slide 45: Why Fast Timing?
Notes: First, I want to highlight the importance of fast timing electronics.

## Slide 46: Why Fast Timing? Explained through Time of Flight (ToF) system
W. Badgett et al., Precision Time-of-Flight at the Fermilab Testbeam Facility (2018)
Notes: We will look at time of flight system as an example.
When the speed of the particle is close to the speed of light, resolving small difference between v and c determines the momentum of the particle.
You can see what time scale we are on from the bottom plot.
We will look a few exemplary detector systems which can utilize this high resolving power.

## Slide 47: An Electron-Ion Collider Study(2019)
EIC is the local particle collider at BNL with of .
Notes: In the Electron-Ion collider in Brookhaven, the momentum resolution of the detector system will be at best 1% at 50 Giga electron volts. Looking back at our diagram of Pion and Kaons, for example, this resolution indeed corresponds to a region of sub picosecond time resolution. So it is evident that we need a fast timing electronics corresponding to the high performance detector system.

## Slide 48: LHCb Detector Performance(2014)
The LHCb collaboration, https://arxiv.org/pdf/1412.6352.
Notes: LHCb is another example of detector system with high momentum resolution, again at best 1% at 50 Giga electron volts and higher. And as I said, this indicates that we need a sub picosecond fast timing electronics.

## Slide 49: Fermilab Test Beam Facility
E. Angelico, Development of Large-Area MCP-PMT photo-detectors for a Precision Time-of-Flight System at the Fermilab Test Beam Facility(2020)
Further development of the system is now taking place in hands of Joe Pastika.
Notes: Fianally, Fermilab test beam facility is the testbed of our chips and detector systems pushing fast timing boundaries.
Evan Angelico had set up a prototype time of flight system using our fast timing chip, psec4, and micro channel plate photomultiplier tube based detector which we call LAPPDs, the setup is shown in the diagram.
Further development of the system is now taking place in hands of Joe Pastika, Fermilab.

## Slide 50: PSEC4 ASIC Measurement and Calibration
Notes: Now, I will briefly discuss the structure of the fast timing chip we have right now.

## Slide 51: Sample time calibration
Time between samples are determined by a VCDL.
Each element of the VCDL has different time offset.
Notes: Time difference between samples are determined by a voltage-controlled delay line, which is an array of transistors, usually MOSFETs, which a signal propagates through the array at a desired rate.
However, no chip manufacturing process is perfect, so each element of the VCDL has different time offset.
It is necessary to measure each time offset to correctly sample a signal.

## Slide 52
1. Measure many events of a sine wave.
2. Sum vs. Difference of two adjacent samples, over all events, form an ellipse.
3. Time offset can be determined from the coefficients.
determined by eccentricity and rotation.
Chart: 
 | 0.5 | 0.63049 | 0.735 | 0.79272 | 0.79215 | 0.73342 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504
Chart: 
 | 0.79272 | 0.79215 | 0.73342 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378
Chart: 
 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378 | 0.79097 | 0.73022 | 0.62364
Chart: 
 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378 | 0.79097 | 0.73022 | 0.62364 | 0.49243 | 0.36274 | 0.26037
Input Voltage
Time
Event 1
Event 2
Event 3
Event 4
Noise  fainter, more spread curve.
Nonlinearity  distorted curve
Notes: We have developed a method to measure time offset of each sample.
1. Measure many events of a sine wave.
2. Plot Summation vs. Difference of two adjacent samples, over all events, should form an ellipse.
3. Time offset can be determined from the coefficients.
The diagram explains which event corresponds to which dot in the ellipse plot.
When you think about it, the plot does not have to be on two adjacent samples, but samples which are m samples apart. This way the effect of voltage noise of each sample on the time offset is smaller.
In other words, the sampled curve is more like a smooth ellipse as m gets larger.
However, the time difference cannot be larger than one fourth of the period of the sine wave, which in our case corresponded to m equal to about 10.
When we look at the right ellipse plot,
Higher voltage Noise results in fainter, more spread curve.
Nonlinearity of the overall system results in distorted curve

## Slide 53: Voltage linearization
It is necessary to reconstruct voltage from ADC value. The curve differs for each capacitor.
1. V_ped is set to a voltage of interest, 0.0v-1.2v
2. PSEC4 is left in sampling mode for a few cycles, so that all capacitors are set to V_ped. ()
3. Each register is read. Each curve corresponds to a capacitor.
Linearizable Domain
~0.75V
Notes: What bothered us next is the fact that the capacitors, shown in a green circle in the diagram on the right, lose or gain charges during the short time between signal input and readout, so *the 12-bit number from each ADC and the actual input voltage appear not linear, and they differ for each capacitor.*
It is necessary to reconstruct input voltage value from 12-bit ADC readout value. We use the curves in the left plot for this, which is a differing characteristic for each capacitor in the array.
The way we measured this curve is very straightforward.
1. V_ped, in the red circle, is an independent variable which is represented by x axis in the left plot, is set to a voltage of interest, 0.0v-1.2v
2. PSEC4 is left in sampling mode for a few cycles, so that all capacitors are set to V_ped. The signal to noise ratio in this case is 0.5 millivolts.
3. Each register is read. Each curve corresponds to a capacitor.

## Slide 54: Performance Measurement
Same signal fed into two different channels of the same readout board.
1. measured for many events.
2. Distribution of acquired.
Depends on the source
  Sin
  Pulse/square
Depends on algorithm determining .
PSEC4
Signal
Ch. 1
Ch. 2
Trigger
Chart: Ch. 1 Voltage[V]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: Ch. 1 Voltage[V]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: Time[ns]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: Time[ns]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
t=0 when the VCDL loop starts
Notes: After the forementioned calibration process,
We finally want to measure the performance of the chip, and one way to do so is to measure *time distribution of the sampled signal when sampling the same waveform many times.*
We set up an experiment where Same signal is fed into two different channels of the same readout board.
Then, delta t , the phase difference, is measured for each event the way described in figure on the right side.
1. measured for many events.
2. Distribution of acquired.
However, one should be aware that delta t depends on the signal source and the algorithm determining where the pulse starts.
After the forementioned calibration process,
We finally want to measure the performance of the chip, and one way to do so is to measure *time distribution of the sampled signal when sampling the same waveform many times.*
We set up an experiment where Same signal is fed into two different channels of the same readout board.
Then, delta t , the phase difference, is measured for each event the way described in figure on the right side.
1. Δ𝑡 measured for many events.
2. Distribution of Δ𝑡 acquired.
However, one should be aware that delta t depends on the signal source and the algorithm determining where the pulse starts.

## Slide 55
[ps]
# of Events
Chart: 
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: 
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: 
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Chart: 
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Notes: We have acquired timing resolution below 5ps through this method. This histogram displays ten thousand events and the standard deviation is about 3 picoseconds.
Delta T histogram

## Slide 56: Setup over a distance
Two channels of each chip is used: one for signal, one for synchronization sine wave.
Sync. is a component of the total timing resolution.
PSEC4
Detector 1
Trigger
PSEC4
Detector 2
Trigger
WR
WR
Phase Sync’d
Sine wave
1ps
Synchronization via optical fiber
Ch. 1
Ch. 2
Ch. 1
Ch. 2
>100m
F. Girela-Lopez, J. Lopez-Jimenez, M. Jimenez-Lopez, R. Rodriguez, E. Ros and J. Díaz,
IEEE 1588 High Accuracy Default Profile: Applications and Challenges in IEEE Access, vol. 8, pp. 45211-45220, 2020
Notes: Same can be done for signal sources a long distance apart, for detector systems like time of flight system.
Two channels of each chip is used: one for signal, another for synchronization sine wave. So in total four channels are used.
The sync. Sine wave is generated by a special module, called white rabbit, which outputs phase synchronized sine waves Over long distance like over kilometers, via optical fiber communication. The phase jitter of this sine wave is way below 1ps for our application.
Sync. is a component of the total timing resolution of detector systems like this.

## Slide 57
t=0 when the sine wave crosses zero.
Chart: Detector 1 Voltage[V]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
 | 0.5 | 0.63049 | 0.735 | 0.79272 | 0.79215 | 0.73342 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378 | 0.79097 | 0.73022 | 0.62364 | 0.49243 | 0.36274 | 0.26037 | 0.20572 | 0.20966 | 0.2714 | 0.37867 | 0.51009 | 0.6395 | 0.74114 | 0.79476 | 0.7897 | 0.72695 | 0.61902 | 0.48739 | 0.35827 | 0.25737 | 0.20478 | 0.21097 | 0.2747 | 0.3833 | 0.51513 | 0.64394 | 0.7441 | 0.79566 | 0.78835 | 0.72362 | 0.61438 | 0.48235 | 0.35385 | 0.25444 | 0.20393 | 0.21236 | 0.27807 | 0.38796 | 0.52016 | 0.64835 | 0.747 | 0.79647
Chart: Time[ns]
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.6 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84 | 0.87 | 0.9 | 0.93 | 0.96 | 0.99 | 1.02 | 1.05 | 1.08 | 1.1100000000000001 | 1.1399999999999999 | 1.17 | 1.2 | 1.23 | 1.26 | 1.29 | 1.32 | 1.35 | 1.38 | 1.41 | 1.44 | 1.47 | 1.5 | 1.53 | 1.56 | 1.59 | 1.62 | 1.65 | 1.68 | 1.71 | 1.74 | 1.77
 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2125 | 0.2325 | 0.2775 | 0.3225 | 0.375 | 0.415 | 0.4625 | 0.5 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.525 | 0.5 | 0.4625 | 0.415 | 0.375 | 0.3225 | 0.2775 | 0.2325 | 0.2125 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
 | 0.5 | 0.63049 | 0.735 | 0.79272 | 0.79215 | 0.73342 | 0.62821 | 0.49748 | 0.36724 | 0.26344 | 0.20674 | 0.20843 | 0.26817 | 0.37407 | 0.50504 | 0.63501 | 0.7381 | 0.79378 | 0.79097 | 0.73022 | 0.62364 | 0.49243 | 0.36274 | 0.26037 | 0.20572 | 0.20966 | 0.2714 | 0.37867 | 0.51009 | 0.6395 | 0.74114 | 0.79476 | 0.7897 | 0.72695 | 0.61902 | 0.48739 | 0.35827 | 0.25737 | 0.20478 | 0.21097 | 0.2747 | 0.3833 | 0.51513 | 0.64394 | 0.7441 | 0.79566 | 0.78835 | 0.72362 | 0.61438 | 0.48235 | 0.35385 | 0.25444 | 0.20393 | 0.21236 | 0.27807 | 0.38796 | 0.52016 | 0.64835 | 0.747 | 0.79647
Notes: Again, this is how we determine delta t and t=0.
As I said, different algorithms can be used for different waveforms. In this case, the variation of delta t will increase by factor of 2, compared to close distance setup. Because the timing uncertainty of both the signal channel and the synchronization channel must be considered.

## Slide 58: Future <1ps chip
Notes: Moving toward the end of this talk, I want to assert that now is the right time for a 1 picosecond timing chip.

## Slide 59: Time is right for a 1-psec timing chip
  Must optimize three aspects:
    Signal rise time
    voltage noise of samples
    sampling time jitter/uncertainty
Adopted from Stefan Ritt “The role of analog bandwidth and signal-to-noise in timing for waveform digitizing“
Notes: We hope the new chip is better in three aspects we have discussed before in this talk.
    Signal rise time
    voltage noise of samples
    sampling time jitter/uncertainty
    As we can see from the equation at the bottom, these three are the factors contributing to the overall timing resolution.
    And we will see that the improvements can be achieved by using more modern chipmaking processes.

## Slide 60
Great deal of work needs to be done but clear that 65nm CMOS technology superior characteristic to 130nm and older
Smaller process nodes give intrinsically faster transistors
Alessandra Pipino, Design of Analog Circuits in 28nm CMOS Technology for Physics Applications (2016)
Some selected results from literature:
(Romanova and Barzdenas: “A Review of Modern CMOS Transimpedance Amplifiers for OTDR Applications”, 2019)
Improved signal rise time
Improved or equal voltage noise of samples
Notes: Great deal of work needs to be done but
One thing sure is that smaller process nodes give faster transistors.
This implies potentially
Improved signal rise time
Improved or equal voltage noise of samples

## Slide 61: Improved packaging also important
Chi-Tsung Chiu, Sung-Mao Wu and Chi-Ping Hung, "High speed electrical performance comparison between bump with RDL and wire bond technologies," Proceedings of the 4th International Symposium on Electronic Materials and Packaging, 2002., 2002
 | (ps) observed for 35ps risetime input pulse | Degradation (%)
Case A (wirebonded) | 65ps | 86%
Case B (flip-chip + RDL) | 42ps | 20%
 |  | Degradation (%)
Case A (wirebonded) | 65ps | 86%
Case B (flip-chip + RDL) | 42ps | 20%
Notes: Also, we can improve the rising time of the pulse through better packaging, since shorter trace length results in lower degradation of rising time.

## Slide 62: Time is right for a 1-psec timing chip!
Notes: These three combined, here is the final table of specifications we expect for the new chip.
One final assertion of our team is that
1-psec timing chip is possible and it is the right time for it.

## Slide 63: Nonlinearity

## Slide 64: Introduction
Fermilab Test Beam Facility (FTBF) – Supports a wide program of research and detector R&D
  2 Beamlines (MTest and MCenter) – can provide particles from 120 GeV protons to secondaries of ~200 MeV to 60 GeV
Beam is available ~9 months a year (roughly October through June)
Notes: The Fermilab Test Beam Facility sits in Fermilab Batavia site and Supports a wide program of research and detector R&D
.
The main beam is 120GeV proton with secondaries of various energies. Beam is available all year except summers.

## Slide 65: FTBF Beamline Details
4 second beam spill every 60 seconds, available 24/7
~1000 to 900,000 particles per spill
MTest
  120 GeV primary protons
  1-66 GeV secondary beam
  ~2cm spot size
  1-4 week runs
MCenter
  Secondary beam
  Two tertiary beamlines down to 200 MeV
  longer term experiments
Notes: This is a few

## Slide 66: Time of Flight System Specifications
Distance: ~80m
Timing resolution: ~5ps
W. Badgett et al., Precision Time-of-Flight at the Fermilab Testbeam Facility (2018)
New permanent facility infrastructure available to all Users

## Slide 67: Apparatus: LAPPD
Adopted from Evan Angelico (2020)

## Slide 68: Apparatus: LAPPD
Adopted from Evan Angelico (2020)

## Slide 69: Apparatus: LAPPD
Adopted from Evan Angelico (2020)

## Slide 70: Timing Resolution of LAPPD
A. V. Lyashenko et al., Performance of Large Area Picosecond Photo-Detectors (LAPPDTM)(2020)
Single photoelectron timing resolution: ~50ps
Particle timing resolution: ~5ps ()

## Slide 71: Apparatus: ACC/ACDC System
Adopted from Eric Oberla’s talk at ps workshop 2014

## Slide 72: Instrumentation Layout - MTest
Proposed LAPPD stations
~80 m
Readout PC
WR Switch
ACC
ACDC
ACC
ACDC
ACC
ACDC
TP Zen
TP Zen
TP Zen
ACDC
ACDC

## Slide 73: otsdaq Integration
K.Biery et. al, The Fermilab Test Beam Facility Data Acquisition System Based on otsdaq
otsdaq is a “ready-to-use” Data Acquisition (DAQ) system that is also capable of configuring and controlling individual experiments through a GUI.

## Slide 74: Leakage
Most leak current comes from vdd & gnd of the gate of the switch. However, the amount of it depends on the voltage of the signal line.
Hold time is calculated using Vdd-gnd pulse as a signal, sampling vdd, and measuring how long does ff corner takes to reach 0.9vdd. (This is the worst case for leak current.)
Equilibrium point depends on the process variation of the switch. The voltage of the capacitor will decay to that point, and the decay time also depends on the variation.

## Slide 75: Citations(All from the doc lib)
Preliminary Specifications for a 1-Picosecond Resolution ASIC for the FTBF TOF System
A Modular Data Acquisition System using the 10 GSa/s PSEC4 Waveform Recording Chip
DEVELOPMENT OF LARGE-AREA MCP-PMT PHOTO-DETECTORS FOR A PRECISION TIME-OF-FLIGHT SYSTEM AT THE FERMILAB TEST BEAM FACILITY
Measurement Noise and Time-Base Calibration in ACDC Data