## Slide 1: PSEC Collaboration
Y.M. Richmond Yeunga , Evan Angelicod, Andrew Arzaca, Gordon Chen a, Ahan Dattaa, Troy Englandb, Henry J. Frischa, Nathan Gehla, Mary Heintza, Sumin Kima, Arjun Kulkarnia , Ava Lalicha , Nathaniel J. Pastikab, Jinseo Parkd, Hector D. Rico-Anilesc, Paul M. Rubinovb,
March 31, 2026
aEnrico Fermi Institute, the University of Chicago, 933 East 56th Street, 60637, Chicago, IL, USA
bFermi National Accelerator Laboratory, 60510, Batavia, IL, USA
cNorth Central College, 30 N. Brainard Street, 60540, Naperville, IL, USA
dStanford University, 450 Jane Stanford Way, 94305, Stanford, CA, USA

## Slide 2: Time-of-flight Particle Identification
LAPPD
LAPPD
Readout Electronics
Software
Using the relation , we can solve for the particle’s mass:
Beam
Given a relativistic particle with relativistic velocity , the time of flight is:
By reconstructing the mass with time-of-flight, we can identify the particle.
*in units of ns and feet
Notes: Using time-of-flight, we can reconstruct a particle’s mass and thus identify the particle.

## Slide 3: The picosecond regime
Picosecond timing enables the search for new physics at colliders: Electron Ion Collider (EIC), LHCb and more.
Test beams enable the calibration and development of other novel detector technologies
Better timing resolutions allow for better image resolution for Positron Emission Tomography: <10 ps is a long-standing goal of the industry.
Contours of detector timing resolution needed to distinguish 68.27% of pions and kaons as a function of momentum and path-length.
XCAT Brain phantom at 1/100th dose

## Slide 4: PSEC5/6 – An Application Specific Integrated Circuit (ASIC)
Timing detectors have demonstrated resolutions as low as 5 picoseconds.
More detectors in series = better resolution
However, the timing uncertainty from the electronics would remain.
Number of detectors N | Timing resolution
2 | 5
3 | 4.08
4 | 3.53
5 | 3.16
6 | 2.89
Number of detectors N | 
2 | 5
3 | 4.08
4 | 3.53
5 | 3.16
6 | 2.89
Current electronics gets to ~15 picoseconds. We aim to achieve a resolution of ~1 ps.
PSEC5 ASIC

## Slide 5: PSEC6 Specifications
Process | 65nm TSMC
Signal to Noise | 1000
Sampling Rate | 40GSa/s (5GSa/s)
Fast Buffer Length | 6.4ns
Slow Buffer Length | 204.8ns
Analog Bandwidth | 4.9 GHz
Channels/Chip | 8
Area | 2.6 mm2
Max. Readout Rate | 40KHz
Institutions | UChicago & Fermilab
Switched Capacitor Array (SCA) based waveform-sampling ASIC
Designed in TSMC 65nm process
Requires stable 5.12 GHz sampling clock  PLL
First 10 GHz PLL in 65 nm for HEP experiment
Notes: PSEC6 is a Switched Capacitor Array, or SCA, based waveform-sampling ASIC designed in TSMC 65 nanometer. It’s maximum sampling rate is 40 Gigasamples per second with a baseline rate of 5 Gigasamples per second, which requires a 5 Gigahertz stable sampling clock. Thus, we need to make a PLL, which is the first 10 gig PLL in 65 nm for HEP experiment to our knowledge.

## Slide 6: 10.24 GHz Phase Locked Loop (PLL) in 65nm CMOS
65nm CMOS is one of the most commonly used processes in High Energy physics.
A PLL in 65nm CMOS has not been achieved in the High Energy Physics community.

## Slide 7: Design of a Modular Test/Readout System
FPGA based readout system
Uses AMD’s Kria K26 - Custom Zynq™ UltraScale+™ MPSoC
Customizable DUT board design
8 Channel 65MSPS ADC readout to FPGA
Kria K26 SOM
DUT Board

## Slide 8: Low Dose TOF PET
Goal is factor of > 1000 reduction in radiation dose
Parameter | Value
Time Resolution (σₜ) | 0.1 ns
Axial Resolution (σ_z) | 0.3 mm
Tangential Resolution (σ_φ) | 0.3 mm
Radial Resolution (σ_r) | 7.3 mm
Spatial Resolution (FBP) | 0.57 mm FWHM
Spatial Resolution (EM) | 0.51 mm FWHM
Pixel Resolution | 0.2 mm
Gamma Energy | 511 keV
Dose Reduction Goal | >1000×