## Slide 1: 10.24 GHz PLL for PSEC6, a 40 GSa/s Waveform Sampling ASIC in 65nm CMOS
Ahan Dattaa, Evan Angelicod, Andrew Arzaca, Gordon Chen a, Troy Englandb, Henry J. Frischa, Nathan Gehla, Mary Heintza, Sumin Kimd, Ava Lalicha , Nathaniel J. Pastikab, Jinseo Parkd, Hector D. Rico-Anilesc, Paul M. Rubinovb, Y.M. Richmond Yeunga,
March 19, 2026
aEnrico Fermi Institute, the University of Chicago, 933 East 56th Street, 60637, Chicago, IL, USA
bFermi National Accelerator Laboratory, 60510, Batavia, IL, USA
cNorth Central College, 30 N. Brainard Street, 60540, Naperville, IL, USA
dStanford University, 450 Jane Stanford Way, 94305, Stanford, CA, USA

## Slide 2: Outline
Motivation for Picosecond Timing Resolution
PSEC5 and PSEC6
10.24 GHz Phase Locked Loop (PLL) Overview
LC Voltage-Controlled Oscillator (VCO)
Divider Blocks
Phase Frequency Detector (PFD)
Charge Pump (CP)
Loop Filter (LPF)
PLL Simulation Results
Outlook

## Slide 3: Time-of-flight Particle Identification
LAPPD
LAPPD
Readout Electronics
Software
Using the relation , we can solve for the particle’s mass:
Beam
Given a relativistic particle with relativistic velocity , the time of flight is:
By reconstructing the mass with time-of-flight, we can identify the particle.
*in units of ns and feet
Notes: Using time-of-flight, we can reconstruct a particle’s mass and thus identify the particle.

## Slide 4: Primary goal – Picosecond Timing Resolution
[1]Stefan Ritt; The role of analog bandwidth and signal-to-noise in timing for waveform digitizing; Timing Workshop, Chicago April 28th 2011,
https://psec.uchicago.edu/workshops/fast_timing_conf_2011/system/docs/18/original/ritt_analog_bw.ppt
Therefore, an improved Δt can be achieved by:
Low Noise (from samples)
High Analog Bandwidth
Minimizing Sampling time jitter
High Sampling Rate
Where Sampling Rate and Bandwidth
Require fast, stable sampling clock
Notes: The main factors affecting timing resolution are noise, sampling time jitter, sampling rate and analog bandwidth. The last two require a fast, stable sampling clock

## Slide 5: PSEC5 and PSEC6
PSEC5 is a pathfinder 40 GSa/s waveform sampling ASIC that was taped out in August 2024
Made to test the new sampling architecture
For the first submission, we decided to not include a PLL
It didn’t perform as we hoped, particularly due to issues with the clock dividers
 We added a redesign of the clock dividers + PLL to PSEC5, calling it PSEC6
PSEC5 Full Chip layout:
Notes: PSEC5 was primarily intended to test the sampling architecture, and thus we only included an oscillator without a PLL. Unfortunately, PSEC5 didn’t work as expected due to issues with the clock dividers. We both fixed the clock dividers and added a PLL to PSEC5, calling it PSEC6.

## Slide 6: PSEC6 Specifications
Process | 65nm TSMC
Signal to Noise | 1000
Sampling Rate | 40GSa/s (5GSa/s)
Fast Buffer Length | 6.4ns
Slow Buffer Length | 204.8ns
Analog Bandwidth | 4.9 GHz
Channels/Chip | 8
Area | 2.6 mm2
Max. Readout Rate | 40KHz
Institutions | UChicago & Fermilab
Switched Capacitor Array (SCA) based waveform-sampling ASIC
Designed in TSMC 65nm process
Requires stable 5.12 GHz sampling clock  PLL
First 10 GHz PLL in 65 nm for HEP experiment
Notes: PSEC6 is a Switched Capacitor Array, or SCA, based waveform-sampling ASIC designed in TSMC 65 nanometer. It’s maximum sampling rate is 40 Gigasamples per second with a baseline rate of 5 Gigasamples per second, which requires a 5 Gigahertz stable sampling clock. Thus, we need to make a PLL, which is the first 10 gig PLL in 65 nm for HEP experiment to our knowledge.

## Slide 7: Design Targets for the 10.24 GHz PLL
Stability across process, voltage, and temperature (PVT) variation
Jitter, ps
Duty Cycle, within 5% of 50% for SCA function
Power, no greater than 20 mW typically
Settling Time, tune voltage settling times ~ human timescales
Finite Width Eye Diagram  Jitter
Notes: The design targets for the PLL are as follows. Primarily, we need the PLL to be stable across process variations. Secondly, we need the PLL jitter to be much less than a picosecond. Furthermore, we need a duty cycle near 50% for proper operation of the SCAs, and we want power under 20mW with at least human timescale settling.

## Slide 8: Phase Locked Loop (PLL)
Block diagram for 10.24 GHz PLL
const.
Linear approximation:
Loop Filter (LPF)
Phase Frequency Detector (PFD)
Charge Pump (CP)
Voltage-Controlled Oscillator (VCO)
Clock Dividers
C1
R
C2

## Slide 9: 10.24 GHz LC VCO
L
C
10.24 GHz LC VCO design provided by Fermilab
In simulation,
Across process, simulated frequency range of 9.75-11.02 GHz
PLL designed around 10.24 GHz LC VCO

## Slide 10: PSEC6 Divider Architecture
PSEC6:
Redesigned for robustness
New
The clock path is CMOS  CML  CMOS

## Slide 11: Current Mode Logic (CML) Buffer
Purpose of this stage is to reduce swing and wave shape into a square wave
Current Sink
Resistors
Input Transistors
Single differential pair with large current source
CML Buffer
CML Divider
CML CMOS
Level Two Divider x3
Level Three Divider x2

## Slide 12: Level One CML Divider  CML D Flip Flop
Divides the frequency by two (hard at 10.24 GHz!) using Two flip-flop (DFF) topology
Transistor sizing had to be tuned to balance input capacitance of the “sense” stage with the “latch” stage strength
Single DFF layout
Differential CML DFF schematic
Level One CML Divider schematic
Sense
Latch
CML Buffer
CML Divider
CML CMOS
Level Two Divider x3
Level Three Divider x2

## Slide 13: CML -> CMOS Converter
Converts the 5.12 GHz clock signal from CML to CMOS logic Two stage amplifier to maximize gain-bandwidth product
Converts 5.12 GHz clock to CMOS logic for compatibility with SCA sampling
CML Buffer
CML Divider
CML CMOS
Level Two Divider x3
Level Three Divider x2

## Slide 14: Level Two TSPC Clock Divider
Divide by two circuit used from 5.12 GHz  1.2 GHz
Standard True Single-Phase Clock (TSPC) Divider is smaller and lower power than CML divider
TSPC divider balances speed, power consumption, and layout area for middle frequencies
CML Buffer
CML Divider
CML CMOS
Level Two Divider x3
Level Three Divider x2

## Slide 15: Level Three Clock Divider
Divide by two from 1.2 GHz  20 MHz using single flip-flop topology
Is the final division stage before the phase-frequency detector
Simple low-power single-FF divider for the slower final division stages
CML Buffer
CML Divider
CML CMOS
Level Two Divider x3
Level Three Divider x2

## Slide 16: Phase Frequency Detector (PFD)
Generates the phase error signal for PLL feedback
Uses And-Or-Not digital standard cell for the reset path
Uses standard cell D flip flops, buffers, and gates for stability
[3] Behzad Razavi, Design of Analog CMOS Integrated Circuits, 2nd ed. (New York: McGraw-Hill, 2016).
Active Low Reset Path
The PFD is the primary feedback generator, and is therefore highly symmetric and designed for fast signal paths

## Slide 17: Charge Pump (CP)
Converts phase error into current to drive the loop filter
Using only-NMOS current-steering design to improve matching for the up and down paths
CP current is configurable with a current bias input
The charge pump must be symmetric since it contributes primarily to the jitter, power consumption, and stability of the loop

## Slide 18: Loop Filter (LPF)
Works as a transconductance low pass filter, smoothing out the output of the charge pump
Directly holds the value of the tuning voltage, and is thus a critical component to tune for minimal jitter
Is critical for loop stability, settling time, and jitter
The LPF was carefully tuned to balance phase margin, damping factor, and the loop frequency
800-1600 Ω
120 pF
12 pF

## Slide 19: PLL Simulation Results: Vtune Convergence
The tuning voltage converges, and thus the PLL locks
Finite thickness of Vtune is from a mysterious 20.48 GHz “harmonic noise”
Vtune converges to 744.6 mV, roughly mid-rail (0.6V)  good tuning range

## Slide 20: PLL Simulation Results: Harmonic Noise
There is a 20.48 GHz 41 mV peak-to-peak harmonic in the tuning voltage. Why?
We expect this noise to “alias to DC” in the sampling.
20.48 GHz harmonic noise is strange, but won’t affect sampling jitter

## Slide 21: PLL Simulation Results: Specifications
PLL Characteristic | Value
Average Total Power *† | 
RMS Jitter *†‡ | 
Duty Cycle of Sampling Clock * | 
Charge Pump Current | 
Characteristic Damping Time Scale * | 
PLL Characteristic | Value
Average Total Power *† | 
RMS Jitter *†‡ | 
Duty Cycle of Sampling Clock * | 
Charge Pump Current | 
Characteristic Damping Time Scale * | 
*Ranges given by process variation
†Max value given by devices away from mean
‡Frequency integration bounds for jitter are 10 MHz-11GHz
Our PLL satisfies our design specifications!
Since the charge pump current and LPF are tunable, we expect to always get the PLL to lock across PVT variations
To further reduce jitter, we can severely underdamp the PLL at the cost of increased damping time , since that is not a critical parameter

## Slide 22: Summary and Future – March 2026
We have developed a 10.24 GHz PLL in TSMC 65nm with 194 fs jitter
Tapeout for PSEC6 is scheduled for April 2026
We are currently finishing floorplan and layout of the full PLL
We expect the chip back for physical testing in July

## Slide 23: Supplementary Slides

## Slide 24: Alias to DC?
Time of Sample (5.12 GHz)
The frequency variation per sample is the same
In other words, the 20.48 GHz jitter is “averaged out”
20.48 GHz harmonic noise on Vtune doesn’t affect the sampling jitter

## Slide 25: How is 40 GS/s achieved with a 10 GHz clock?
Interleaving SCAs, delayed clock
We only need a 5GHz sampling clock for 40 Gsa/s sampling rate
Dual Edge Triggered Flip Flops allow for the use of both clock edges for sampling
Triggering on the rising edge
Using both edges

## Slide 26: PLL Corner Results: Vtune Convergence
Green = Typical; Red = Fast; Yellow = Slow.
Converges in all corners

## Slide 27: VCO Output
1.2 V peak-to-peak differential sine wave  Needs to be divided

## Slide 28: CML Buffer Output
~10.24 GHz
0.4 V – 0.8 V swing depending on corner

## Slide 29: Level One Divider Output
600-800 mV peak-to-peak swing across PVT variations
~5.12 GHz Frequency

## Slide 30: CMLCMOS Buffer Output
5.12 GHz Square Wave
Duty cycle within 5% of 50% across all PVT variations
Used for the sampling clock!

## Slide 31: PFD Output
~200 ps reset path delay
Phase Error

## Slide 32: Ideal Phase-Frequency Detector
Left: a PFD implemented as two flip flops and a reset with a Charge Pump, Right: Behavior when Clock A is ahead of Clock B
“Up”
“Down”
[3] Behzad Razavi, Design of Analog CMOS Integrated Circuits, 2nd ed. (New York: McGraw-Hill, 2016).

## Slide 33: LPF Layout
The C1 capacitor is 120 pF and C2 is 12 pF, both implement using MIMCAPS
The resistor can be tuned between 850 and 1650 Ohms
Tunable Resistor layout
Pass Gate
Polysilicon Tuning Resistor
Main Filter Resistor
C1
C2
R

## Slide 34: Improved Clock Divider Architecture
PSEC5:
IR Drop
Small
Single Ended
~15 MHz
PSEC6:
Redesigned for robustness
New

## Slide 35
Sampling Buffer Architecture
Uses different sized buffers for main chain and channel input
Multiple buffers to minimize the parasitic capacitance from the buffers themselves
Channel
Channel
Channel
Channel
Channel
Channel
Channel
Channel
PLL
Sampling Clock ~5.12 GHz
Multi-stage buffering required to drive 5.12 GHz clock across 8 channels

## Slide 36: Architecture: Fast and Slow SCAs
Fast Banks x4:
  64 samples each
  1.6 ns Buffer length
  Can be configured to run sequentially
Chart: Time [ns]
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4 | 4.2 | 4.4000000000000004 | 4.5999999999999996 | 4.8 | 5 | 5.2 | 5.4 | 5.6 | 5.8 | 6
Signal (Slow Bank) | 0.00053624 | 0.0028827 | 0.010784 | 0.022583 | 0.062327 | 0.1382 | 0.28673 | 0.49189 | 0.73028 | 0.92587 | 1.0061 | 0.93102 | 0.73772 | 0.51052 | 0.33758 | 0.27169 | 0.33537 | 0.51282 | 0.74075 | 0.93391 | 1.0059 | 0.92497 | 0.72881 | 0.48882 | 0.28197 | 0.13886 | 0.063164 | 0.02677 | 0.010479 | 0.0025898 | 0.0088129
Threshold | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
A
B
Chart: Time [ns]
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4 | 4.2 | 4.4000000000000004 | 4.5999999999999996 | 4.8 | 5 | 5.2 | 5.4 | 5.6 | 5.8 | 6
Fast Bank A | 0.49048 | 0.73025 | 0.92675 | 1.0058 | 0.93032 | 0.73916 | 0.50816 | 0.33716
Fast Bank B | 0.51585 | 0.73608 | 0.9294 | 1.0054 | 0.92325 | 0.73551 | 0.49321 | 0.28063
Propagation delay ~800ps
Hold delay ~800ps
10bit counter
Slow Bank:
  Up to 1024 samples
  204.8 ns Buffer length
  Captures the entire signal.
A solution to the fast sampling and long analog buffer problem:
Ref. [2] Jinseo Park, Design of an 8 Channel 40 GS/sec 20 mW/Channel Waveform Sampling ASIC in 65 nm CMOS, PM 2024

## Slide 37: Controlling the Switches: Clock Signal
Clocks in electronics are just square waves with a known frequency:
“High”
“Low”
Threshold
Crystal Oscillators are extremely precise but cannot reach GHz frequencies.
RLC Circuits can be arranged to oscillate if they meet the Barkhausen Criteria:
Loop Gain = ,
Loop Phase =
Vout:
LCs can oscillate at the GHz range, but the frequency is under-determined.
E.g. 160 MHz – 6.25 ns period:
0.1ps jitter
[3] Behzad Razavi, Design of Analog CMOS Integrated Circuits, 2nd ed. (New York: McGraw-Hill, 2016).

## Slide 38: Phase Margin, Trade-offs
Bode plot: Loop Phase, and Loop Gain
Old Phase margin was 4 deg – It was very unlikely to be stable! We correct for this by increasing the size of C1 and R. We now have a 47 deg margin.
C2 adds an extra pole that reduces the ripples in Vtune, but destroys the phase margin
Phase Margin is the degrees of loop phase above -180 (where the loop is unstable), when the loop gain is 0. Mathematically:
Where:

## Slide 39: PLL Dynamics
Convergence of Vtune, and thus the VCO frequency, in time
Consider an ideal PLL with a linear VCO:
The Phase detector compares the reference with the divided VCO output:
And a loop filter with Impedance (Z):
From the loop filter, the control voltage takes:
Taking the derivative of the phase error:
A PLL is a PI loop tuned by the resistance and capacitance

## Slide 40: Damped, Driven Oscillator
Define (the frequency offset as seen as the PFD) and the loop gain
Differentiating:
A mechanical 2nd order oscillator can be described as:
A direct comparison gives the natural frequency and damping factor:
Where is underdamped – causes ringing,
is overdamped – overshoot, and is critically damped.
Ringing from an underdamped PLL.
Damping factor is critical to determine settling time

## Slide 41: Stability
The First Convergence looked healthy, but the Laplace domain was concerning:
The forward path (PFD -> Charge Pump -> Loop Filter -> VCO) gives:
With , we get the open loop transfer function:
And a closed-loop transfer function of
Nyquist plots for a PLL open-loop transfer function. [5]
The loop is unstable if the contour hits (-1,0)
Open loop analysis: Will the loop be stable?
Closed Loop analysis: If the loop is stable, how does it respond?
[3] Behzad Razavi, Design of Analog CMOS Integrated Circuits, 2nd ed. (New York: McGraw-Hill, 2016).

## Slide 42: Extra pole from C2
Yes, C2 also introduces a pole from its own impedance.
This would call adjustments in the loop parameters. (PLL is now third-order)
However, keeping C2 >> C1: We are using a ratio of 1:10, we can keep the second order approximation.
[13] Xiaoran Wang, “A 10 GHz Low-Jitter Cryogenic PLL for Quantum Applications in 22 nm” (presentation, CPAD 2024, Oak Ridge National Laboratory / University of Tennessee, Knoxville, TN, November 19, 2024),

## Slide 43: Particle ID
Using Time of Flight, one can identify pions from kaons from their momenta.
For relativistic particles (p >> m) of the same momenta (:
Contours represent detector timing resolution required to distinguish 68.27% of pions and kaons by momenta and path length
[11] Angelico, E; Development of LAPPDs for a Precision ToF System at the Fermilab Testbeam Facility (Doctoral Dissertation, University of Chicago, 2020)

## Slide 44: LAPPDs
MCPs: Small pores (high spatial resolution)
Charged Particle -> Cherenkov -> electrons
Cherenkov radiation: “Sonic boom” for light in a medium
Spatial Resolution along the anode stripline is reconstructed by measuring the time difference of signals on the same line
An LAPPD, by component.
[12] Incom, Inc., “LAPPD – Large Area Picosecond Photodetector,” (webpage), accessed December 1, 2025,

## Slide 45: Full system block diagram
Detector
Device Board
Control Board
Reconstruction
Software
Data Analysis
FPGA
Block Diagram of PSEC5 [2]

## Slide 46: References
[1] Stefan Ritt; The role of analog bandwidth and signal-to-noise in timing for waveform digitizing; Timing Workshop, Chicago April 28th 2011 https://psec.uchicago.edu/workshops/fast_timing_conf_2011/system/docs/18/original/ritt_analog_bw.ppt
[2]Park, J., et al. 2025. “Design of an 8-Channel 40 GS/s 20 mW/ sampling ASIC in 65nm CMOS.” Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1072 (2025)
[3]Behzad Razavi, Design of Analog CMOS Integrated Circuits, 2nd ed. (New York: McGraw-Hill, 2016).
[4] Niner, E; “Fermilab Test Beam Facility” , Fermilab ACE Science Workshop, June 2023
[5] Inami, K., et al. “A 5 ps TOF-counter with an MCP–PMT.” Nuclear Instruments and Methods in Physics Research Section A 566, no. 1 (2006): 52–56.
[6] Unknown Author. “Chapter 1: Introduction.” Lecture slides, PS412, Embry-Riddle Aeronautical University, undated. https://physicsx.erau.edu/Courses/CoursesF2025/PS412/Lectures/Chapter%201%20Introduction.pdf
[7] D. A. Stricker-Shaver, S.Ritt, B. J. Pichler; Novel Calibration Method for Switched Capacitor Arrays Enables Time Measurements with Sub-Picosecond Resolution https://arxiv.org/pdf/1405.4975

## Slide 47
[8] Oberla, E; Charged Particle Tracking in an Optical Time Projection Chamber (Doctoral Dissertation, University of Chicago, 2015)
[9] Yeung, et al. “Design of an 8-channel 40 GS/s 20 mW/Ch waveform sampling ASIC in 65nm CMOS”, FAST 2025, Elba. https://indico.cern.ch/event/1445926/contributions/6400606/
[10] Arzac et al, “A Modular Test System for the PSEC5 40 GS/s waveform sampling ASIC” FAST 2025, Elba
[11] Angelico, E; Development of LAPPDs for a Precision ToF System at the Fermilab Testbeam Facility (Doctoral Dissertation, University of Chicago, 2020)
[12] Incom, Inc., “LAPPD – Large Area Picosecond Photodetector,” (webpage), accessed December 1, 2025,
[13] Xiaoran Wang, “A 10 GHz Low-Jitter Cryogenic PLL for Quantum Applications in 22 nm” (presentation, CPAD 2024, Oak Ridge National Laboratory / University of Tennessee, Knoxville, TN, November 19, 2024),